The B50 motor has to be offset 1-9/16" to the left in the frame in order to put on more than a 2 " wide tire.  Bsa designed these things originally as a 250cc and apparently didn't imagine that wider tires might be desireable.  So I needed motor mounting capability on my jig with infinite adjustability.  I made up some upstands using 1-1/2" angle slotted for 1/2" carriage bolt and fitted with a 5/8" threaded rod welded on.  At the top is another angle bolted to motor, with a 5/8" id tube welded on.  I can move the upstand anywhere on the fixture I want, and adjust the motor mount up and down.  Clamped to fixture with carriage bolt.