Front suspension axle location

# Text boxes

Plan

Front track ca. 44” – 48”

Rack fixed to axle; no bump steer but need sliding spline column

Rose joint to chassis

Hairpin trailing arm allows steering arm / rack to pass through

Reinforcing fillet

Axle

Side elevation

Pivot pin (~14mm) with mount assembly on centre of axle – this engages a sliding block (guides attached to chassis) and allows pivot (single wheel bump), vertical movement (two-wheel bump) but not lateral movement.

Rose joints allow castor tuning